## Slide 1: Assembly Language Programming
Course Code: 0052
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | 4 | Week No: | 4 | Semester: | Summer 21-22
Lecturer: | Md. Faruk Abdullah Al Sohan; faruk.sohan@aiub.edu |  |  |  | 
Course Title: Computer Organization and Architecture

## Slide 2: Content
1. Creating, Assembling and executing assembly language program.
2. By the end of this lesson we will be able to write simple but interesting assembly program.

## Slide 3: Overview
Four Steps
  Learn Syntax
  Variable declarations
  Introduction of basic data movement
  Program organization: Code, Data and stack
Assembly language instructions are so basic. So, I/O is much harder unlike high-level languages.
We Use DOS functions for I/O as they are easy to invoke and faster
A program is must be converted to machine language before execution

## Slide 4: Assembly Language Syntax
Assembly language is not case sensitive, however, we use upper case to differentiate code from rest of the text.
Statements:
  Programs consist of statements (one per line)
  Each statement can be any of following types:
    Instruction that are translated into machine code
    Assembler directives that instruct the assemble to perform some specific task:
      Allocating memory space for variables
      Creating procedure

## Slide 5: Fields
  Instructions and directives can have up to four fields:
    Name Operation Operand(s) comment
    START MOV CX,5 ; initialize counter
    **[Fields must appear in this order]
    MAIN PROC [ creates a Procedure]
    At least one blank or tab character must separate the fields

## Slide 6: Name Field
Name: it is used for instruction levels, procedure names and variable names.
  The assembler translates names into variable names.
  Can be 1 to 31 characters long and consists of letter , digit and special characters.
  Embedded blanks are not allowed.
  Names may not begin with number.
  UPPERCASE and lowercase in name are same.
  Examples: COUNTER1, $1000, Done?, .TEST
    Illegal names TWO WORD, 2AB, A45.28, ME &YOU

## Slide 7: Solve the Following
Which of the following names are legal in IBM PC assembly language?
  TWO_WORDS
  TwoWOrDs
  ?1
  .@?
  $145
  LET’S_GO
  T = .

## Slide 8: Operation Field
Operation field contains a symbolic operation code (opcode).
The assembler translates a symbolic opcode into a machine language.
Opcode symbols often describe the operations function (e.g. MOV, ADD, SUM etc..).
In assembler directive, the operation field contains pseudo operation code (pseudo-ops).
Pseudo-ops are NOT translated into machine code. they simply tell the assembler to do something.
  e.g. PROC pseudo-op is used to create procedure.

## Slide 9: Operand Field(cont’d…)
Operand field species the data that are to be acted on by the operation.
An instruction may have zero, one or two operands. e.g.
First operand is Destination (i.e. register or Memory location)
  some instruction do not store any result
Second operand is Source and its not usually modified by instruction
NOP | No operands; does nothing
INC AX | Adds one to the contents of AX
ADD WORD1,2 | Add 2 to the contents of WORD1

## Slide 10: Comment Field
Comment: put instruction into the context of program.
Comment field of a statement is used to say something about what the statement does?
Semicolon ( ; ) marks in the beginning of this field
Assembler ignores anything typed after “ ; “
** Comment is very important in assembly language and it is almost impossible to understand assembly code without comment.
** Commenting is considered as good programming practice

## Slide 11: Program Data
Processor operates only on binary data.
So, the assembler MUST translate all data representation into binary numbers.
In assembly program, we may express data as binary, decimal or hex numbers and even characters.
Numbers:
  Binary: a binary number is written as bit string followed by the letter B or b (e.g. 1010B)
  Decimal: A decimal number is a string of decimal digits. It ends with optional “D” or “d” (e.g. 1234).
  Hex: A hex number begins with a decimal digit and ends with the letter H or h (e.g. 12ABh).
Characters:
  Character strings must be enclosed with single or double quotes.
  e.g. ‘A’ or “hello” is translated into ASCII by assembler. So, there is no difference between ‘A’ or 41h or 65d.

## Slide 12: Program Data
Which of the following are legal numbers? if they are legal tell whether they are Binary, decimal or hex numbers?
    246
    246h
    1001
    1,001
    2A3h
    FFFEh
    0Ah
    Bh
    1110b
Solve the Following

## Slide 13
We use a variable to store values temporarily.
Each variable has a data type and is assigned a memory address by the program.
We will mostly use DB (define byte) and DW(define word) variables.
Byte Variables: In the following , the directive associates a memory byte to ALPHA and initialize it to 4. A “?” mark can be used for uninitialized byte. The range of values in a byte is 2^8 or 256
    Name DB Initial_value
    ALPHA DB 4
Word Variables: Similar to byte variable and the range of initial values is 2^16 or 65536.
    Name DW Initial_value
    WRD DW -2
Variables

## Slide 14
Array is just a sequence of bytes or words.
i.e. to define a three-byte array, we write
  B_ARRAY DB 10h, 20h, 30h
  Name B_ARRAY is associated with first byte, B_ARRAY+1 with second and B_ARRAY+2 with third.
B_ARRAY | 200 | 10h
B_ARRAY+1 | 201 | 20h
B_ARRAY+2 | 202 | 30h
Array

## Slide 15
  Create a word array (named MY_W_ARRAY) table of which the starting address is 500 and values are 2000,323,4000 and 1000.
Array Exercise

## Slide 16
MY_W_ARRAY | 500 | 2000
MY_W_ARRAY+2 | 502 | 323
MY_W_ARRAY+4 | 504 | 4000
MY_W_ARRAY +6 | 506 | 1000
MY_W_ARRAY DW 2000,323,4000,1000
Solution

## Slide 17
High and Low bytes of Word: Sometimes we may need to refer to the high and low bytes of a word variable. i.e. if we define,
    WORD1 DW 1234H
    the low byte of WORD1 contains 34h (symbolic address: WORD1) and High byte contains 12h (symbolic address: WORD1+1).
Character string: An array of ASCII codes.
  LETTER DB ‘ABC’
  LETTER DB 41h,42h,43h [ UPPERCASE]
  MSG DB `HELLO’, 0Ah, 0Dh, ’$’ [combination is also possible]
  MSG DB 48h,45h,4Ch,4Ch,4Fh,0Ah,0Dh,24h
Array (Cont.)

## Slide 18
Using a symbolic name for constant quantity make the assembly code much easier.
EQU (Equates): Assign a name to a constant
  e.g. LF EQU 0Ah [LF= 0Ah]
  ( LF=0Ah is applicable to whole code after assigning)
  PROMPT EQU ‘Type Your Name’
  **No memory is allocated for EQU names**
Named Constant

## Slide 19
MOV is used to transfer data between registers, register and memory-location or move number directly into register or memory location.
Syntax: MOV destination, source
        MOV AX, WORD1 [reads Move WORD1 to AX]
Before | After
0006 | 0008
AX | AX
0008 | 0008
WORD1 | WORD1
Instructions: MOV
        **Copy of WORD is sent to AX

## Slide 20
Source Operand | General Register | Segment Register | Memory location | Constant
General Register | Yes | Yes | Yes | No
Segment Register | Yes | No | Yes | No
Memory location | Yes | Yes | No illegal: MOV W1,W2 | No
Constant | Yes | No | Yes | No
Legal Combinations of Operands for MOV

## Slide 21
What is the value of BX and A after MOV BX,A ?[assume value of A is 24h]
Using previous values, find the value of AX and BX from MOV AX, BX
Tell us whether the following instructions are legal or illegal?
    MOV DS,AX
    MOV DS,1000h
    MOV CS,ES
    MOV W1,DS
    MOV W1,B1
Solve the Following

## Slide 22
MOV is used to exchange the contents between two registers or register and memory-location.
Syntax: XCHG destination, source
XCHG AH, BL
[reads exchange value of AH with BL]
Before |  | After | 
1A | 00 | 05 | 00
AH | AL | AH | AL
00 | 05 | 00 | 1A
BH | BL | BH | BL
Instructions: XCHG

## Slide 23
Source Operand | General Register | Memory location
General Register | Yes | Yes
Memory location | Yes | No illegal: XCHG W1,W2
Legal combinations of operands for XCHG

## Slide 24
What is the value of BX and A after XCHG BX,A?[assume value of A is 15h].
Also find, AX and A after MOV AX,A ?
Using previous values, find the value of AX and BX from XCHG AX, BX?
Tell us whether the following instructions are legal or illegal?
    XCHG W1,W2
    XCHG AX,W1
Solve the following

## Slide 25: Using Register, MOV AX, W2 XCHG AX,W2 MOV W1, AX
XCHG or MOV operation is not allowed between memory locations. So, What could be the way out?
Solution

## Slide 26
ADD is used to add content of two registers, register and memory-location or add a number to register or memory location.
Syntax: ADD destination, source
        ADD WORD1,AX [reads Add AX to WORD1]
        **Copy of WORD1 is added with content of AX and stored in WORD1
Before | After
01BC | 01BC
AX | AX
0523 | 06DF
WORD1 | WORD1
Instructions: ADD

## Slide 27
Source Operand | General Register | Memory location
General Register | Yes | Yes
Memory location | Yes | No illegal: ADD W1,W2
Constant | Yes | Yes
Legal Combinations of Operands for ADD

## Slide 28
What is the value of BX and A after ADD BX,A ?[assume value of BX is 5h and A is 9h]
using previous values[AX=9h], find the value of AX and BX from ADD AX, BX
Tell us whether the following instructions are legal or illegal?
  ADD B1,B2
  ADD AL,56H
Solve the Following

## Slide 29
SUB is used to subtract content of two registers, register and memory-location or subtract a number from register or memory location.
Syntax: SUB destination, source
        SUB AX,DX [reads Subtract DX from AX]
        **Subtracts the content of DX from AX and stored in AX.
Before | After
0000 | FFFF
AX | AX
0001 | 0001
DX | DX
Instructions: SUB

## Slide 30
Source Operand | General Register | Memory location
General Register | Yes | Yes
Memory location | Yes | No illegal: SUB W1,W2
Constant | Yes | Yes
Legal Combinations of Operands for ADD

## Slide 31
What is the value of BX and A after SUB BX,A ?[assume value of BX is F and A is 9h]
Using previous values[AX=9h], find the value of AX and BX from SUB AX, BX
Tell us whether the following instructions are legal or illegal?
  SUB B1,B2
  SUB AL,56H
Solve the Following

## Slide 32
INC is used to add 1 to the contents of a register or memory-location.
Syntax: INC destination
        INC WORD1 [reads Add 1 to WORD1]
        ** 1 is added to WORD1 and result is stored in WORD1
Before | After
0002 | 0003
WORD1 | WORD1
Instructions: INC

## Slide 33
What is the value of BX and A?[assume BX=3h and A=9h]
INC BX
INC A
Solve the Following

## Slide 34
DEC is used to subtract 1 from the contents of a register or memory-location.
Syntax: DEC destination
        DEC WORD1 [reads subtract 1 from WORD1]
        ** 1 is subtracted from BYTE1 and result is stored in BYTE1
Before | After
FFFE | FFFD
WORD1 | WORD1
Instructions: DEC

## Slide 35
What is the value of BX and A?[assume BX=3h and A=9h]
DEC BX
DEC A
Solve the Following

## Slide 36
NEG is used to negate the contents of the destination
NEG does this by replacing the contents by its two’s complement.
Syntax: NEG destination
        NEG BX [reads negate the contents of BX]
        ** The content of BX is replaced with its two’s complement
Before | After
0002 | FFFE
BX | BX
Instructions: NEG

## Slide 37
What is the value of BX and A? [assume BX=3h and A=9h]
NEG BX
NEG A
Solve the Following

## Slide 38
The operand of the preceding two-operand instruction MUST be same type. (i.e. both bytes or words). Thus,
  MOV AX,BYTE1 ; its illegal
  MOV AH,’A’ ; legal
  MOV AX,’A’ ; legal if source is a word
Agreement of Operator

## Slide 39
Statement | Translation
B = A | MOV AX,A MOV B,AX ** A direct memory move in illegal
A = 5-A | MOV AX,5 SUB AX,A MOV A,AX or NEG A ADD A,5
A=B-2*A | MOV AX,B SUB AX,A SUB AX,A MOV A,AX
Translation of High-Level Language to Assembly Language

## Slide 40: Program Structure
A program Consist of
  Stack
  Data
  Code
Each part occupies memory segments. Program segment is translated into memory segment by assembler.
The size of code and data of a program can be specified by memory model using .MODEL directive
    .MODEL Memory_model
    .MODEL SMALL [Code in ONE segment and Data in one segment]

## Slide 41: Stack Segment
Allocate a block of memory (stack area) to store the stack.
The stack area should be big enough to contain the stack at its maximum size.
Declaration:
    .STACK size
    .STACK 100H
    ** Allocates 100 bytes for stack area reasonable size for most applications
    ** If size is omitted 1KB is allocated for stack area.

## Slide 42: Data Segment
Contains all the variable definitions and sometimes Constant definitions (constant does not take any memory).
To declare data segment .DATA directive is used followed by variable and constant declaration.
            .DATA
            WORD1 DW 2
            BYTE1 DB 1
            MSG DB ‘THIS IS A MESSAGE’
            MASK EQU 10010001B

## Slide 43: Code Segment
Contains the program’s instructions
Declaration:
  .CODE name [name is optional]
    There is no need of name in SMALL program
Inside a code segment, instructions are organized as procedures.
  name PROC
  ; body of the procedure
  name ENDP
  Here name = name of the procedure. PROC and ENDP are pseudo-ops

## Slide 44: Program Structure
    .MODEL SMALL
    .STACK 100H
    .DATA
    ; data definitions here
    .CODE MAIN
    MAIN PROC
    ;instructions go here
    MAIN ENDP
    ;other procedures go here
    END MAIN
    The last line of the program should be the END directive, followed by the name of main procedure

## Slide 45: Instruction: INT (Appendix C)
INT: Interrupt option stops the continuous progress of an activity or process.
Syntax:
  INT interrupt_number
***A particular function is requested by placing a function number in the AH register and invoking INT 21h .
*** INT 21h functions expect input values to be in certain registers and return output values to other registers
Function Number | Routine | Input | Output
1 | single-key input | AH=1 | AL = 0 if no input or ASCII of character
2 | single-character output | AH=2 | DL=ASCII of display char AL= ASCII of display char
9 | character-string output | AH=9 | 

## Slide 46: The First Program
Task: Write a program to read a character from the keyboard and display the same at the beginning of next line.
  Lets start by displaying a question (“?”) mark for the user input

## Slide 47: The Solution
    .MODEL SMALL
    .STACK 100H
    . CODE
    MAIN PROC
    ; display prompt to the user
    MOV AH,2 ; display character function
    MOV DL,’?’ ; character is ‘?’
    INT 21H ; display the DL char (?)
    ;input a character
    MOV AH,1 ; read character function
    INT 21H ; character is in AL
    MOV BL,AL ; save input to BL reg
    ;go to new line
    MOV AH,2 ; display character function
    MOV DL,0Dh ; carriage return
    INT 21H ; execute carriage return
    MOV DL,0Ah ; line feed to display
    INT 21h ; execute Line feed
    ; display character
    MOV DL, BL ; retrieve character
    INT 21h
    ;return to DOS
    MOV AH,4Ch ; terminate the currant process and transfer
    control to invoking process
    INT 21h ; termination the execution of program
    return control to DOS
    MAIN ENDP
    END MAIN

## Slide 48: Programming Steps
.ASM file
Assembler
.OBJ file
Linker
.EXE file
Editor
Assemble source program
Link Object program
Create source program

## Slide 49: Instruction: LEA
LEA: Load Effective address
    LEA destination, source
LEA puts copy of the source offset address into the destination.
i.e. LEA DX, MSG ; will load address of MSG to DX

## Slide 50: Program Segment Prefix (PSP)
PSP contains information about the program to facilitate the program access in this area
DOS places its segment number in both DS and ES before program execution
Usually, DS does not contain the segment number of the data segment.
Thus, a program with data segment will start with these two instruction
    MOV AX,@DATA [name of data segment define in .DATA]
    MOV DS,AX

## Slide 51: HW: Solve the Following
Write a program to print HELLO! on the screen
Write a program that can convert the user input character in UPPERCASE like below
Example:
  ENTER A LOWER-CASE LETTER: a
  IN UPPERCASE IT IS: A

## Slide 52
References
Assembly Language Programming and Organization of the IBM PC, Ytha Yu and Charles Marut, McGraw Hill, 1992. (ISBN: 0-07-072692-2).
https://www.whoishostingthis.com/resources/assembly-language/

## Slide 53
Books
Assembly Language Programming and Organization of the IBM PC, Ytha Yu and Charles Marut, McGraw Hill, 1992. (ISBN: 0-07-072692-2).
Essentials of Computer Organization and Architecture, (Third Edition), Linda Null and Julia Lobur
W. Stallings, “Computer Organization and Architecture: Designing for performance”, 67h Edition, Prentice Hall of India, 2003, ISBN 81 – 203 – 2962 – 7
Computer Organization and Architecture by John P. Haynes.